## Slide 1: ME 497R – Mentored Research
Samuel Nasman
Notes: Why?
To learn more about aircraft design and optimization
  I haven’t had much experience with these sorts of problems, and so it’s been a tremendous learning experience.
What?
2-dimensional airfoils (wing sections; panel method)
Airframe design (vortex lattice method)
Optimizing a wing to minimize induced drag (VLM and an optimizer)
Transition: let’s take a look at 2-dimensional airfoils

## Slide 2
Notes: We want to figure out the properties of this airfoil
Employ a panel method
  make a bunch of panels
  Assume inviscid flow and the Kutta condition at the trailing edge, among other important assumptions
  Model shape of the airfoil using solutions to the Laplace equation
    For Xfoil.jl, we use vortices
  Calculate the circulation which is proportional to the lift, drag, etc.

## Slide 3
Notes: Calculate dimensionless coefficients across a range of angles of attack.
  Increasing angle of attack increases lift and drag until stall
    XFoil actually includes corrections that predict stall to a certain extent
    At stall lift decreases
    Drag increases sharply
    SKIP: at high alpha, r x F may partially explain

## Slide 4
Re =
Notes: Reynolds number is ratio of inertial forces to viscous forces
  For inviscid flows, mu approaches 0 and Re approaches infinity

## Slide 5
Notes: Xfoil assumptions
Inviscid irrotational flow / kutta condition
  Struggles at accurate predictions for high angle of attack (flow separation)

## Slide 6
Notes: Thick airfoils generate smaller lift coefficients, but have softer stall
Extremely thin airfoils have numerical instability. Possible explanations
  Leading edge may trip flow separation
  Panels so close together may be too close to r=0

## Slide 7
Notes: Increasing camber shifts airfoil polars
For low angles of attack, cambered airfoils have higher lift/drag ratios
  Flaps and slats to increase lift when increasing angle of attack isn’t practical.

## Slide 8: Airframe Analysis
Notes: Now lets look at an airframe. How do we analyze it?
Vortex Lattice Method
  Can’t just use panel method because of wing tip vortices
  Vortex filaments for variable circulation
VortexLattice.jl
  Aspect ratio
  Tail volume and Stability
    Note how in this picture we have a large horizontal stabilizer and a small one. How does that affect the aircraft?
  limitations

## Slide 9
Lift / Drag Coefficient Ratio
Aspect Ratio
Notes: Increasing the length of the wing increases the lift to drag ratio
Practical considerations often override

## Slide 10
Notes:   Tail volume is, roughly speaking, the ratio of the aerodynamic influence of the tail to the influence of the wing.
  Tails that are larger or further from the aircraft’s center of gravity have a larger affect on aircraft stability.

## Slide 11
Notes: Change in moment with respect to alpha
Change in roll with respect to beta

## Slide 12
Notes: Change in yaw with respect to beta
Change in pitching moment with respect to alpha (note the significantly smaller scale)

## Slide 13
Notes: Limitations of VLM
Small angles of attack
Flat plate solution (thin wing)

## Slide 14
Wing Optimization
Notes: - Gradient based optimizers calculate numerical derivatives

## Slide 16
Notes: Problem: optimizer is struggling to find a practical solution.
Impose monotonicity.

## Slide 17
Notes: Increase number of panels

## Slide 18
25x6, sd = 0.003539906737094895
4x6, sd = 0.012817921294912426
Notes: The chord distribution is direction proportional to the circulation
Comparison to the analytical solution looks promising!

## Slide 19: Future Work
Optimizer requires ball-park initial chord distribution in order to find analytical solution. Explore better-defining feasible space.
Optimize twist rather than chord.
Look-up table to predict stall.
Splines and Sine-spacing to decrease number of design variables.

## Slide 20
THANK YOU